The ARM Architecture
Architektura ARM

---
Přehled architektur ARM

---
Data Sizes and Instruction Sets
Velikosti dat a instrukční soubor
- ARM je 32-bitová architektura
- Von-Neumannova architektura (společná paměťová oblast pro program i data)
- Velikosti datových objektů:
  - Byte ... 8 bitů
  - Halfword … 16 bitů (2 byty)
  - Word ... 32 bitů (4 byty)
- Implementována jedna ze dvou nebo obě instrukční sady
  - 32-bitová ARM instrukční sada
  - 16-bit Thumb (redukovaná) instrukční sada
- Jazelle jádra navíc umí přímo spustit Java bytecode (Android std. Aplikace,...)
[Speaker Notes: The cause of confusion here is the term “word” which will mean 16-bits to people with a 16-bit background. In the ARM world 16-bits is a “halfword” as the architecture is a 32-bit one, whereas “word” means 32-bits. Java bytecodes are 8-bit instructions designed to be architecture independent. Jazelle transparently executes most bytecodes in hardware and some in highly optimized ARM code. This is due to a tradeoff between hardware complexity (power consumption & silicon area) and speed.]

---
Processor Modes
Operační režimy
ARM podporuje sedm operačních režimů
  - User : neprivilegovaný režim, běh standardních uživatelských úloh
  - FIQ : Fast Interrupt – nastaven při vstupu do obsluhy rychlého přerušení (nejvyšší priorita, externí vstup)
  - IRQ : Interrupt – nastaven při vstupu do obsluhy standardního přerušení – externí události, události interních periferií...
  - Supervisor : výchozí stav RESET a po provedení instrukce Software Interrupt
  - Abort : obsluha chyby přístupu do paměti (mimo mapovanou paměť, adresa nesoudělná s délkou slova...)
  - Undef : obsluha chyby při výskytu nedefinované instrukce
  - System : privilegovaný režim, používá stejné registry jako režim User
[Speaker Notes: The Programmers Model can be split into two elements - first of all, the processor modes and secondly, the processor registers. So let’s start by looking at the modes. Now the typical application will run in an unprivileged mode know as “User” mode, whereas the various exception types will be dealt with in one of the privileged modes : Fast Interrupt, Supervisor, Abort, Normal Interrupt and Undefined (and we will look at what causes each of the exceptions later on). NB - spell out the word FIQ, otherwise you are saying something rude in German! One question here is what is the difference between the privileged and unprivileged modes? Well in reality very little really - the ARM core has an output signal (nTRANS on ARM7TDMI, InTRANS, DnTRANS on 9, or encoded as part of HPROT or BPROT in AMBA) which indicates whether the current mode is privileged or unprivileged, and this can be used, for instance, by a memory controller to only allow IO access in a privileged mode. In addition some operations are only permitted in a privileged mode, such as directly changing the mode and enabling of interrupts. All current ARM cores implement system mode (added in architecture v4). This is simply a privileged version of user mode. Important for re-entrant exceptions because no exceptions can cause system mode to be entered.]

---
The ARM Register Set
Soubor registrů ARM
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
FIQ
IRQ
SVC
Undef
Abort
User Mode
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
Viditelné registry
Skryté registry
FIQ
IRQ
SVC
Undef
Abort
r0
r1
r2
r3
r4
r5
r6
r7
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
Viditelné registry
Skryté registry
User
IRQ
SVC
Undef
Abort
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
FIQ Mode
IRQ Mode
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
Viditelné registry
Skryté registry
User
FIQ
SVC
Undef
Abort
r13 (sp)
r14 (lr)
Undef Mode
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
Viditelné registry
Skryté registry
User
FIQ
IRQ
SVC
Abort
r13 (sp)
r14 (lr)
SVC Mode
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
Viditelné registry
Skryté registry
User
FIQ
IRQ
Undef
Abort
r13 (sp)
r14 (lr)
Abort Mode
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
Viditelné registry
Skryté registry
User
FIQ
IRQ
SVC
Undef
r13 (sp)
r14 (lr)
[Speaker Notes: This animated slide shows the way that the banking of registers works. On the left the currently visible set of registers are shown for a particular mode. On the right are the registers that are banked out whilst in that mode. Each key press will switch mode: user -> FIQ ->user -> IRQ -> user ->SVC -> User -> Undef -> User -> Abort and then back to user. The following slide then shows this in a more static way that is more useful for reference]

---
Register Organization Summary
Přehled organizace registrů
User
FIQ
IRQ
SVC
Undef
Abort
User
mode
r0-r7,
r15,
and
cpsr
User
mode
r0-r12,
r15,
and
cpsr
User
mode
r0-r12,
r15,
and
cpsr
User
mode
r0-r12,
r15,
and
cpsr
User
mode
r0-r12,
r15,
and
cpsr
Thumb state
Low registers
r8
r9
Thumb state
High registers
r10
r11
r12
r13 (sp)
r13 (sp)
r13 (sp)
r13 (sp)
r13 (sp)
r14 (lr)
r14 (lr)
r14 (lr)
r14 (lr)
r14 (lr)
spsr
spsr
spsr
spsr
spsr
Pozn.: Režim System používá registrovou sadu jako režim User
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
r15 (pc)
cpsr
r0
r1
r2
r3
r4
r5
r6
r7
[Speaker Notes: This slide shows the registers visible in each mode - basically in a more static fashion than the previous animated slide that is more useful for reference. The main point to state here is the splitting of the registers in Thumb state into Low and High registers. ARM register banking is the minimum necessary for fast handling of overlapping exceptions of different types (e.g. ABORT during SWI during IRQ). For nested exceptions of the same type (e.g. re-entrant interrupts) some additional pushing of registers to the stack is required.]

---
The Registers
Vlastnosti registrů
ARM obsahuje 37 registrů s šířkou slova 32 bitů
  - 1 program counter
  - 1 current program status register
  - 5 saved program status registers
  - 30 registrů pro obecné použití
Dostupnost registrů závisí na operačním módu
V každém režimu jsou dostupné registry
  - společná sada r0-r12 (kromě FIQ, tam jsou vlastní r8-r12)
  - individuální r13 (stack pointer, sp) a r14 (link register, lr, návratová adresa)
  - program counter, r15 (pc)
  - current program status register, cpsr
Privilegované režimy (kromě System) mají přístupný
  - individuální spsr (saved program status register)
[Speaker Notes: The ARM architecture provides a total of 37 registers, all of which are 32-bits long. However these are arranged into several banks, with the accessible bank being governed by the current processor mode. We will see this in more detail in a couple of slides. In summary though, in each mode, the core can access: a particular set of 13 general purpose registers (r0 - r12). a particular r13 - which is typically used as a stack pointer. This will be a different r13 for each mode, so allowing each exception type to have its own stack. a particular r14 - which is used as a link (or return address) register. Again this will be a different r14 for each mode. r15 - whose only use is as the Program counter. The CPSR (Current Program Status Register) - this stores additional information about the state of the processor: And finally in privileged modes, a particular SPSR (Saved Program Status Register). This stores a copy of the previous CPSR value when an exception occurs. This combined with the link register allows exceptions to return without corrupting processor state.]

---
Program Status Registers
Program Status Registers
Interrupt Disable bits.
  - I = 1: Disables the IRQ.
  - F = 1: Disables the FIQ.
T Bit
  - Architecture xT only
  - T = 0: Processor in ARM state
  - T = 1: Processor in Thumb state
- Mode bits
  - Specify the processor mode
Condition code flags
  - N = Negative result from ALU
  - Z = Zero result from ALU
  - C = ALU operation Carried out
  - V = ALU operation oVerflowed
- Sticky Overflow flag - Q flag
  - Architecture 5TE/J only
  - Indicates if saturation has occurred
- J bit
  - Architecture 5TEJ only
  - J = 1: Processor in Jazelle state
27
31
N Z C V Q
28
6
7
I F T mode
16
23
8
15
5
4
0
24
f
s
x
c
U n d e f i n e d
J
[Speaker Notes: Green psr bits are only in certain versions of the ARM architecture ALU status flags (set if "S" bit set, implied in Thumb state). Sticky overflow flag (Q flag) is set either when saturation occurs during QADD, QDADD, QSUB or QDSUB, or the result of SMLAxy or SMLAWx overflows 32-bits Once flag has been set can not be modified by one of the above instructions and must write to CPSR using MSR instruction to cleared PSRs split into four 8-bit fields that can be individually written: Control	(c)	bits 0-7 Extension	(x)	bits 8-15	Reserved for future use Status	(s)	bits 16-23	Reserved for future use Flags	(f)	bits 24-31 Bits that are reserved for future use should not be modified by current software. Typically, a read-modify-write strategy should be used to update the value of a status register to ensure future compatibility. Note that the T/J bits in the CPSR should never be changed directly by writing to the PSR (use the BX/BXJ instruction to change state instead). However, in cases where the processor state is known in advance (e.g. on reset, following an interrupt, or some other exception), an immediate value may be written directly into the status registers, to change only specific bits (e.g. to change mode). New ARM V6 bits now shown.]

---
Program Counter (r15)
Program Counter (r15)
Při provádění instrukcí ARM:
  - Šířka všech instrukcí je 32 bitů
  - Všechny instrukce musí začínat na adrese dělitelné čtyřmi
  - V důsledku toho je hodnota pc uložena v bitech [31:2] a bity [1:0] mají nedefinovaný obsah
Při provádění instrukcí Thumb:
  - Šířka všech instrukcí je 16 bitů, (některé jsou rozděleny na více slov 16 bitů)
  - Všechny instrukce musí začínat na adrese dělitelné dvěma
  - V důsledku toho je hodnota pc uložena v bitech [31:1] a bity [0:0] mají nedefinovaný obsah
[Speaker Notes: ARM is designed to efficiently access memory using a single memory access cycle. So word accesses must be on a word address boundary, halfword accesses must be on a halfword address boundary. This includes instruction fetches. Point out that strictly, the bottom bits of the PC simply do not exist within the ARM core - hence they are ‘undefined’. Memory system must ignore these for instruction fetches. In Jazelle state, the processor doesn’t perform 8-bit fetches from memory. Instead it does aligned 32-bit fetches (4-byte prefetching) which is more efficient. Note we don’t mention the PC in Jazelle state because the ‘Jazelle PC’ is actually stored in r14 - this is technical detail that is not relevant as it is completely hidden by the Jazelle support code.]

---
Exception Handling
Zpracování výjimek
Při výskytu výjimky je automaticky provedeno:
  - Zkopírování CPSR do SPSR_<mode>
  - Nastavení bitů v CPSR
    - Nastavení ARM stavu
    - Změna režimu
    - Zákaz přerušení
  - Uložení návratové adresy do LR_<mode>
  - Nastavení PC na addresu vektoru
Při návratu z obsluhy musí být provedeno:
  - Obnova CPSR ze SPSR_<mode>
  - Obnova PC z LR_<mode>
Toto smí být provedeno pouze v ARM stavu
FIQ
IRQ
(Reserved)
Data Abort
Prefetch Abort
Software Interrupt
Undefined Instruction
Reset
Tabulka vektorů
0x1C
0x18
0x14
0x10
0x0C
0x08
0x04
0x00
[Speaker Notes: Exception handling on the ARM is controlled through the use of an area of memory called the vector table. This lives (normally) at the bottom of the memory map from 0x0 to 0x1c. Within this table one word is allocated to each of the various exception types. This word will contain some form of ARM instruction that should perform a branch. It does not contain an address. Reset - executed on power on Undef - when an invalid instruction reaches the execute stage of the pipeline SWI - when a software interrupt instruction is executed Prefetch - when an instruction is fetched from memory that is invalid for some reason, if it reaches the execute stage then this exception is taken Data - if a load/store instruction tries to access an invalid memory location, then this exception is taken IRQ - normal interrupt FIQ - fast interrupt When one of these exceptions is taken, the ARM goes through a low-overhead sequence of actions in order to invoke the appropriate exception handler. The current instruction is always allowed to complete (except in case of Reset). IRQ is disabled on entry to all exceptions; FIQ is also disabled on entry to Reset and FIQ.]

---
Conditional Execution and Flags
Instrukční sada
Provedení všech ARM instrukcí může být podmíněno postfixem, který vyjadřuje kombinaci stavových bitů (CPSR)
  - Snižuje počet instrukcí a zejména skoků (rychlost)
  CMP r3,#0 CMP r3,#0
  BEQ skip ADDNE r0,r1,r2
  ADD r0,r1,r2
  skip:
- Defaultně nejsou ovlivňovány stavové bity, toto musí být explicitně vynuceno postfixem “S”. (kromě instrukce CMP)
  loop
   …
   SUBS r1,r1,#1
   BNE loop
r1 = r1 – 1, nastaví příznaky
když je Z nulový pak skoč
[Speaker Notes: Unusual but powerful feature of the ARM instruction set. Other architectures normally only have conditional branches. Some recently-added ARM instructions (in v5T and v5TE) are not conditional (e.g. v5T BLX offset) Core compares condition field in instruction against NZCV flags to determine if instruction should be executed.]

---
Condition Codes
Condition Codes
- Seznam možných podmínek:
    - AL je defaultní a nemusí být uvedena
Not equal
Unsigned higher or same
Unsigned lower
Minus
Equal
Overflow
No overflow
Unsigned higher
Unsigned lower or same
Positive or Zero
Less than
Greater than
Less than or equal
Always
Greater or equal
EQ
NE
CS/HS
CC/LO
PL
VS
HI
LS
GE
LT
GT
LE
AL
MI
VC
Suffix
Description
Z=0
C=1
C=0
Z=1
Flags tested
N=1
N=0
V=1
V=0
C=1 & Z=0
C=0 or Z=1
N=V
N!=V
Z=0 & N=V
Z=1 or N=!V
[Speaker Notes: Condition codes are simply a way of testing the ALU status flags.]

---
Examples of conditional execution
Příklady podmíněných instrukcí
Použití sekvence stejně podmíněných instrukcí
  if (a==0) func(1);
    CMP r0,#0
    MOVEQ r0,#1
    BLEQ func
Použití sekvence různě podmíněných instrukcí
  if (a==0) x=0;
  if (a>0) x=1;
    CMP r0,#0
    MOVEQ r1,#0
    MOVGT r1,#1
Použití podmíněné instrukce CMP
  if (a==4 || a==10) x=0;
    CMP r0,#4
    CMPNE r0,#10
    MOVEQ r1,#0
[Speaker Notes: Sequence of conditional instructions: - no instruction must reset cond code flags - BL corrupts flags so must be last - limit sequence to max 3 or so instrs Can use different condition codes. Give if then else example. Note GCD practical coming later. Conditional compare - resets condition code when executed - compiler will make use of this - can be difficult for a human to understand! Not just for compare, using data processing with condition code and S bit is useful in some circumstances. LDM/LDR instruction cannot set flags due to datapath issues (data comes back only at the very end of the cycle, so there is no opportunity to perform a comparison and set the status flags).]

---
Branch instructions
Instrukce skoku
- Branch :	B{<cond>} label
- Branch with Link :	BL{<cond>} subroutine_label
- Procesorové jádro posune pole offset o 2 bity vlevo, provede znaménkové rozšíření na 32 bitů a přičte k PC
  - Rozsah ± 32 Mbyte
  - Jak provést delší skok?
31
28
27
25
24
23
0
Cond 1 0 1 L Offset
Link bit	0 = Branch
1 = Branch with link
Condition field
[Speaker Notes: PC-relative to allow position independent code, and allows restricted branch range to jump to nearby addresses. How to access full 32-bit address space? Can set up LR manually if needed, then load into PC MOV lr, pc LDR pc, =dest ADS linker will automatically generate long branch veneers for branches beyond 32Mb range.]

---
Data processing Instructions
Instrukce pro operace s daty
Přehled :
  - Aritmetické:	ADD	ADC	SUB	SBC	RSB	RSC
  - Logické:	AND	ORR	EOR	BIC
  - Porovnání	:	CMP	CMN	TST	TEQ
  - Přesun:	MOV	MVN
- Instrukce pracují pouze s registry, NE s pamětí
- Syntaxe:
  <Operation>{<cond>}{S} Rd, Rn, Operand2
    - Instrukce porovnání pouze nastaví příznakové bity – nobsahují Rd
    - Instrukce pro přesun neobsahují Rn
Druhý operand je pro ALU předzpracován jednotkou barrel shifter.
[Speaker Notes: BIC	bit clear ORR	bit set AND	bit mask EOR	bit invert Comparisons produce no results - just set condition codes. CMP	like SUB CMN	like ADD (subtract of a negative number is the same as add) TST	like AND TEQ	like EOR (eor of identical numbers gives result of zero) Generally single-cycle execution (except write to PC and register-controlled shift). Mention ARM NOP & Thumb NOP. Explain RSB and RSC which do subtract in other order (e.g. y-x not x-y) Does not include multiply (separate instr format). No divide - compiler uses run-time library or barrel shifter to perform division. Can combine “S” bit with conditional execution, e.g. ADDEQS r0, r1, r2]

---
The Barrel Shifter
Barrel Shifter
LSL : Logical Left Shift
ASR: Arithmetic Right Shift
Destination
Destination
CF
CF
0
Násobení mocninou 2
Division by a power of 2,
preserving the sign bit
LSR : Logical Shift Right
ROR: Rotate Right
Destination
Destination
CF
CF
...0
Dělení mocninou 2
Bitová rotace s přenosem z LSB do MSB
RRX: Rotate Right Extended
Destination
CF
Bitová rotace přes CF
[Speaker Notes: Rotate left can be implemented as rotate right (32-number), e.g. rotate left of 10 is performed using rotate right of 22. RRX shifts by 1 bit position, of a 33 bit amount (includes carry flag). Very specialized application (e.g. encryption algorithms). Cannot be generated by C compiler. We have used it for 64/64 bit divide. RRX allows you to shift multiprecision values right by one efficiently. Also used in ARM’s MPEG code in a very tricky piece of code. ANSI C does not have a rotate operation (it only has “<<“ and “>>” which are the equivalent of LSL, LSR and ASR). However the ARM compiler recognizes rotate type expresssions and optimizes these to use ROR, e.g. int f(unsigned int a) { return (a << 10) | (a >>22) ; } => MOV a1,a1,ROR #22 Carry flag set out of the shifter for *logical* data processing operations]

---
Using the Barrel Shifter: The Second Operand
Použití Barrel Shifter:
(druhý operand)
Registr, volitelne s operací posunu
  - Hodnota posunu může být:
    - 5 bitová neznaménková hodnota
    - Hodnota spodního bytu jiného registru
  - Používáno pro násobení konstantou
Přímá hodnota
  - osmibitové číslo, rozsah 0-255.
    - Možnost bitové rotace vpravo o sudý počet bitů
  - Umožňuje zadání většího rozsahu 32-bitových konstant (značně omezený)
Result
Operand 1
Barrel
Shifter
Operand 2
ALU
[Speaker Notes: Mention A bus and B bus on 7TDMI core. Give examples: ADD	r0, r1, r2 ADD	r0, r1, r2, LSL#7 ADD	r0, r1, r2, LSL r3 ADD	r0, r1, #0x4E]

---
Immediate constants (1)
Přímé konstanty (1)
ARM instrukce nemůže obsahovat 32 bitovou konstantu
  - Všechny ARM instrukce jsou dlouhé 32 bitů
Instrukce po datové operace mají k dispozici 12 bitů pro druhý operand
- 4 bit rotate value (0-15) is multiplied by two to give range 0-30 in steps of 2
- Rule to remember is “8-bits shifted by an even number of bit positions”.
11
8
7
0
rot
immed_8
x2
Shifter
ROR
[Speaker Notes: Could have used 12 bits directly for immediate value - this would allow 0-4095. But this does not allow any large numbers, which are useful for: base address of memory devices in target system large, but simple hex constants (0x10000) Research has shown there is a need for a large range of small numbers (frequently needed) but also some large numbers. 50% of all constants lie between the range -15 and +15 and 90% lie in the range -511 and +511. Will vary depending on the application. ROR #n is confusing… but can be considered as ROL #32-n Opcode 0xe3a004ff = MOV r0, #0xff, 8 Core rotates 0xff right by 4 pairs of bits => MOV r0, #0xff000000]

---
Immediate constants (2)
Přímé konstanty (2)
- Examples:
- Assembler převede zápis konstant na použití rotací konstanty:
  - MOV r0,#4096	; uses 0x40 ror 26
  - ADD r1,r2,#0xFF0000	; uses 0xFF ror 16
- Bitový doplněk může být zapsán s použitím instrukce MVN:
  - MOV r0, #0xFFFFFFFF	; přeloženo jako MVN r0,#0
Hodnoty, které nemohou být takto převedeny způsobí chybové hlášení překladače
31
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
ror #0
rozsah 0-0x000000ff krok 0x00000001
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
ror #8
rozsah 0-0xff000000 krok 0x01000000
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
ror #30
rozsah 0-0x000003fc krok 0x00000004
[Speaker Notes: Point out that it is 8-bit value shifted to anywhere within the 32-bit word (but must be an even number of bits). Other bits are zeros. Mention that ROR#2,4,6 (not shown) will split the 8-bit immediate with some bits at bottom of word and some at top. mov r0, #256	; mov r0, #0x100 mov r1, #0x40, 30	; mov r1, #0x100 etc. This method of generating constants allows 3073 distinct values, about 25% fewer than if 12-bits were used without modification. They are, however, a much more useful set of values.]

---
Loading 32 bit constants
32-bitové konstanty
Pro obecné použití konstant s vyššími hodnotami je v assembleru zavedena pseudo-instrukce:
  - LDR rd, =const
Která zajistí:
  - Použití MOV or MVN pokud je to možné.
nebo
  - Generování LDR instrukce s adresou relativní k PC, načte hodnotu přímo ze 32b slova z paměti
Příklady:
  - LDR r0,=0xFF	=>	MOV r0,#0xFF
  - LDR r0,=0x55555555	=>	LDR r0,[PC,#Imm12]
    …
    …
    DCD 0x55555555
[Speaker Notes: 26 Literal pools These are constant data areas embedded in the code at the end of assembler modules, and at other locations if specified by the user using LTORG. Data value must not be executed (will probably be an undefined instruction), assembly programmer must ensure this by placing LTORG at an appropriate location. ARM C compilers will handle placement of literal pools automatically.]

---
Multiply
Násobení
Syntaxe:
  - MUL{<cond>}{S} Rd, Rm, Rs	Rd = Rm * Rs
  - MLA{<cond>}{S} Rd,Rm,Rs,Rn	Rd = (Rm * Rs) + Rn
  - [U|S]MULL{<cond>}{S}	RdLo, RdHi, Rm, Rs	RdHi,RdLo := Rm*Rs
  - [U|S]MLAL{<cond>}{S} RdLo, RdHi, Rm, Rs	RdHi,RdLo := (Rm*Rs)+RdHi,RdLo
Čas instrukce
  - Základní instrukce MUL
    - 2-5 cyklů v ARM7TDMI
    - 1-3 cykly v StrongARM/XScale
    - 2 cykly v ARM9E/ARM102xE
  - +1 cykl pro ARM9TDMI (oproti ARM7TDMI)
  - +1 cykl pro součet
  - +1 cykl pro verzi “long”
[Speaker Notes: Variable number of cycles for some processors which implement ‘early termination’. The multiply is faster for smaller values in Rs. ARM7TDMI and ARM9TDMI use 8-bit Booth’s algorithm which takes 1 cycle for each byte in Rs. Terminates when rest of Rs is all zeros or all ones. MUL/MLA don’t need signed/unsigned specified - because they return the low 32-bit of the result which is the same whatever the sign of the arguments. Cycle information is general and specific cores have some specific variations from this, specifically with respect to result delays where accumulation is involved. Refer to TRM for exact details if required. XScale and StrongARM have a split pipeline with multiple execution units - so can issue multiplies in 1 or 2 cycles and continue with following instructions, assuming no resource or result dependencies. XScale can issue MUL/MLA/MULL in one cycle (MLAL requires 2 cycles), providing multiplier is not already in use. Cycle timing is dependent on result latency - the core will stall if an instruction tries to use the result before multiplier has completed. Note that there is no form of the multiply instruction which has an immediate constant operand - registers only. For the interested student - C flag is unpredictable if S is set in architectures prior to V5. MULS/MLAS always take 4 cycles; MULLS, MLALS always take 5.]

---
Single register data transfer
Přesun dat Registr <> Paměť
  LDR	STR	Word
  LDRB	STRB	Byte
  LDRH	STRH	Halfword
  LDRSB	Signed byte load
  LDRSH	Signed halfword load
- Paměť musí podporovat všechny šířky slov
- Syntax:
  - LDR{<cond>}{<size>} Rd, <address>
  - STR{<cond>}{<size>} Rd, <address>
  e.g. LDREQB
[Speaker Notes: Point out destination (reg) first for LDR, but destination (mem) last for STR. Different to Motorola, but it keeps the instruction mnemonic format consistent. Always have register loaded/stored first, then address accessed second Size specifier comes out on MAS (memory access size) signal. Important that memory supports full range of accesses - especially important for writes where only the specified size should be written. Special types of sign extended load - this is needed because ARM registers only hold 32-bit values. Draw diagram. No need for special store instructions though. Instruction cycle timing: STR	LDR 7TDMI	2 cycles	3 cycles 9TDMI	1 cycle	1 cycle - interlock if used in next cycle StrongARM1	1 cycle	1 cycle - interlock if used in next cycle Xscale	1 cycle	1 cycle - interlock if used in next 2 cycles Note size specifier comes after condition code. Link: <address> explained on next slide. Note that load/store instructions never set condition codes.]

---
Address accessed
Adresování
- Adresa pro instrukci LDR/STR je zapsána jako bázový registr plus offset
- Pro přístup WORD a neznaménkový BYTE
  - Přímá hodnota 12 bitů (tzn. 0 - 4095 bytů).
    LDR r0,[r1,#8]
  - Registr bitově posunutý o přímo zadanou hodnotu
    LDR r0,[r1,r2]
    LDR r0,[r1,r2,LSL#2]
- Hodnota může být přičtena nebo odečtena s bázovým registrem:
  LDR r0,[r1,#-8]
  LDR r0,[r1,-r2]
  LDR r0,[r1,-r2,LSL#2]
- Pro halfword a znaménkový halfword / byte, může být offset:
  - Přímá neznaménková osmibitová hodnota (tzn. 0-255 bytů).
  - Registr (bez možnosti bitového posunu).
Možnost pre nebo post modifikace registru
[Speaker Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common. Link: diagram on next slide]

---
Pre or Post Indexed Addressing?
Pre or Post Indexed Addressing?
Pre-indexed: STR r0,[r1,#12]
r0
Offset
Zdrojový registr pro STR
0x5
12
0x5
0x20c
r1
Bázový
Registr
0x200
0x200
Post-indexed: STR r0,[r1],#12
Modifikovaný bázový registr
r1
Offset
0x20c
12
0x20c
r0
Zdrojový registr pro STR
0x5
Původní bázový registr
r1
0x5
0x200
0x200
[Speaker Notes: “!” indicates “writeback” i.e. the base register is to be updated after the instruction. No “!” for post-indexed because post-increment of base register always happens (otherwise the offset field would not be used at all). Give C example: int *ptr; x = *ptr++; Compiles to a single instruction: LDR r0, [r1], #4]

---
LDM / STM operation
LDM / STM operace
Syntaxe:
  <LDM|STM>{<cond>}<addressing_mode> Rb{!}, <register list>
4 adresní módy:
  LDMIA / STMIA	increment po
  LDMIB / STMIB	increment před
  LDMDA / STMDA	decrement po
  LDMDB / STMDB	decrement před
IA
IB
DA
DB
LDMxx r10, {r0,r1,r4}
STMxx r10, {r0,r1,r4}
r4
r4
r1
r1
r0
Rostoucí
adresa
Bázový Registr (Rb)
r10
r0
r4
r1
r4
r0
r1
r0
[Speaker Notes: Always lowest register first. Always ascending memory address order. Uses sequential cycles to take advantage of faster access. ‘addressing_mode’ just determines whether up/down with respect to the base pointer and if value at base pointer address is accessed or skipped. It isn’t possible to add any offset to the base pointer. Note address and registers loaded/stored are the other way around compared with LDM/STM. Note the base pointer is not loaded or stored, unless it is in the reg list.]

---
Software Interrupt (SWI)
Software Interrupt (SWI)
0
31
28
27
24
23
Cond 1 1 1 1
SWI number (ignored by processor)
Podmínka
- Softwarové vyvolání výjimky (přerušení), jediná SW možnost přechodu do privilegovaného módu
- Lze specifikovat 24-bitovou hodnotu, která může být použita obslužnou rutinou
- Syntax:
  - SWI{<cond>} <SWI number>
[Speaker Notes: In effect, a SWI is a user-defined instruction. Used for calling the operating system (switches to privileged mode). SWI number field can be used to specify the operation code, e.g. SWI 1 start a new task, SWI 2 allocate memory, etc. Using a number has the advantage that the O.S. can have different revisions, and the same application code will work on each O.S. rev.]

---
PSR Transfer Instructions
Instrukce pro přesun PSR
- MRS a MSR přesouvá obsah CPSR / SPSR do nebo z obecného registru
- Syntaxe:
  - MRS{<cond>} Rd,<psr> ; Rd = <psr>
  - MSR{<cond>} <psr[_fields]>,Rm ; <psr[_fields]> = Rm
kde
  - <psr> = CPSR or SPSR
  - [_fields] = libovolná kombinace ‘fsxc’
Možnost použití přímé konstanty
  - MSR{<cond>} <psr_fields>,#Immediate
V režimu User mohou být všechny bity CPSR čteny ale zápis je možný pouze u podmínkových bitů (f)
27
31
N Z C V Q
28
6
7
I F T mode
16
23
8
15
5
4
0
24
f
s
x
c
U n d e f i n e d
J
[Speaker Notes: The status registers are split into four 8-bit fields that can be individually written: bits 31 to 24 : the flags field (NZCV flags and 4 unused bits) bits 23 to 16 : the status field (unused in Arch 3, 4 & 4T) bits 15 to 8 : the extension field (unused in Arch 3, 4 & 4T) bits 7 to 0 : the control field (I & F interrupt disable bits, 5 processor mode bits, and the T bit on ARMv4T.) Immediate form of MSR can actually be used with any of the field masks, but care must be taken that a read-modify-write strategy is followed so that currently unallocated bits are not affected. Otherwise the code could have distinctly different effect on future cores where such bits are allocated. When used with the flag bits, the immediate form is shielded from this as bits 27-24 can be considered to be read only. For MSR operations, we recommend that only the minimum number of fields are written, because future ARM implementations may need to take extra cycles to write specific fields; not writing fields you don't want to change reduces any such extra cycles to a minimum. For example, an MRS/BIC/ORR/MSR sequence whose purpose is to change processor mode (only) is best written with the last instruction being MSR CPSR_c,Rm, though any other set of fields that includes "c" will also work.]

---
ARM Branches and Subroutines
ARM skoky a podprogramy
B <label>
  - Relativně k PC, rozsah ±32 MB
BL <subroutine>
  - Uloží návratovou adresu do LR
  - Návrat se provede obnovením PC z LR
  - LR musí být většinou ukládán na zásobník programem
func1
func2
:
:
BL func1
:
:
STMFD sp!,{regs,lr}
:
BL func2
:
LDMFD sp!,{regs,pc}
:
:
:
:
:
MOV pc, lr
[Speaker Notes: This slide shows the way that ARM branch instructions work It also shows the need to stack the LR (using STM/LDM instructions) when making subroutine calls within subroutines.]

---
Thumb
Thumb
Thumb je 16-ti bitová instrukční sada
  - Optimalizována pro výstup překladače C (~65% velikosti ARM kódu)
  - Zlepšuje využitelnost menší kapacity paměti
  - Instrukce jsou interně převáděny na instrukce ARM a takto vykonávány
  - Přepínání mezi ARM a Thumb módem se provede instrukcí BX
Většina instrukcí generovaných překladačem:
Nepoužívá podmíněné instrukce
Stejný cílový registr s operandem
Používá pouze spodní množinu registrů
Konstanty mají omezenou velikost
Inline barrel shifter není použit
0
15
31
0
ADDS r2,r2,#1
ADD r2,#1
32-bit ARM Instruction
16-bit Thumb Instruction
[Speaker Notes: The Thumb instruction set was designed by looking at the instructions produced by the ARM C compiler from real application code to see which instructions were most often used. This subset of instructions was then compressed into 16-bit opcodes to give better code density and better performance from narrow memory A Thumb compatible processor is still a 32-bit processor, but it has the ability to execute either sections of ARM code or sections of Thumb code. The two instruction sets cannot be interleaved though, a special form of branch has to be used to change “state”. The diagram then shows the way that a typical 32-bit ARM instruction might be “compressed” into a 16-bit Thumb one.]

---
Example ARM-based System
Struktura procesoru (MCU)
Peripherals
32 bit RAM
16 bit RAM
Interrupt
Controller
I/O
nIRQ
nFIQ
8 bit ROM
ARM
Core
[Speaker Notes: This slides shows a very generic ARM based design, that is actually fairly representative of the designs that we see being done. On-chip there will be an ARM core (obviously) together with a number of system dependant peripherals. Also required will be some form of interrupt controller which receives interrupts from the peripherals and raised the IRQ or FIQ input to the ARM as appropriate. This interrupt controller may also provide hardware assistance for prioritizing interrupts. As far as memory is concerned there is likely to be some (cheap) narrow off-chip ROM (or flash) used to boot the system from. There is also likely to be some 16-bit wide RAM used to store most of the runtime data and perhaps some code copied out of the flash. Then on-chip there may well be some 32-bit memory used to store the interrupt handlers and perhaps stacks.]

---
AMBA
AMBA
Arbiter
Reset
ARM
TIC
Timer
Remap/
Pause
External
ROM
External
Bus
Interface
Bus Interface
External
RAM
Interrupt
Controller
On-chip
RAM
Decoder
AHB or ASB
APB
System Bus
Peripheral Bus
ACT
  - AMBA Compliance Testbench
PrimeCell
  - ARM’s AMBA compliant peripherals
AMBA
  - Advanced Microcontroller Bus Architecture
ADK
  - Complete AMBA Design Kit
Bridge
[Speaker Notes: AMBA is ARM’s on-chip bus specification. The aims of AMBA are to: Make life easier for Systems designers Standardise the bus interface Reduce the support required from ARM and between internal design teams Allows increased re-use of IP in designs Enable the creation of upgrades and families of devices Why use AMBA not the original ARM Bus Improved Tools support Modularity Upgrading to other ARM cores ADK is ARM’s AMBA design kit. A generic, stand-alone development environment enabling rapid creation of AMBD-based components and designs. ACT is a complete environment for testing compliance to the AMBA spec. The PrimeCell peripherals are a set of AMBA-compliant peripherals that are available for licensing from ARM. They include a UART, real time clock, keyboard & mouse interface, GPIO and a generic IR interface. Consult the ARM website for more details - a selection of reference manuals are also on the technical documentation CD.]

---
Blokové schéma AT91SAM9260

---
Blokové schéma jádra ARM926

---
Vlastnosti AT91SAM9260
Incorporates the ARM926EJ-S™ ARM® Thumb® Processor
- DSP Instruction Extensions, ARM Jazelle® Technology for Java® Acceleration
- 8-KByte Data Cache, 8-KByte Instruction Cache, Write Buffer
- 200 MIPS at 180 MHz
- Memory Management Unit
- EmbeddedICE™, Debug Communication Channel Support
Additional Embedded Memories
- One 32 KByte Internal ROM, Single-cycle Access At Maximum Matrix Speed
- Two 4 KByte Internal SRAM, Single-cycle Access At Maximum Matrix Speed
External Bus Interface (EBI)
Supports SDRAM, Static Memory, ECC-enabled NAND Flash and CompactFlash®
USB 2.0 Full Speed (12 Mbits per second) Device Port
USB 2.0 Full Speed (12 Mbits per second) Host Single Port (1 or 2)

---
Vlastnosti AT91SAM9260
Ethernet MAC 10/100 Base T
- Media Independent Interface or Reduced Media Independent Interface
- 28-byte FIFOs and Dedicated DMA Channels for Receive and Transmit
Image Sensor Interface
Bus Matrix
- Six 32-bit-layer Matrix
- Boot Mode Select Option, Remap Command
Fully-featured System Controller, including
- Reset Controller, Shutdown Controller
- Four 32-bit Battery Backup Registers for a Total of 16 Bytes
- Clock Generator and Power Management Controller
- Advanced Interrupt Controller and Debug Unit
- Periodic Interval Timer, Watchdog Timer and Real-time Timer